## Slide 1
A ONE-HOUR TECHNICAL SESSION FOR RF & RAN ENGINEERS
Deep Reinforcement Learning for RAN Planning & Optimization
How DQN and PPO learn to tune coverage, capacity, mobility, interference, and energy the way an experienced RF engineer would — explained without the math.
60 MINUTES · 21 TOPICS · ZERO EQUATIONS REQUIRED

## Slide 2
02
AGENDA
What We'll Cover in 60 Minutes
00–10 min
Why RAN optimization needs AI now, and what RL actually is
10–25 min
DQN and PPO explained simply, with RAN use cases for each
25–45 min
Deep dives: coverage & capacity, mobility, energy, interference, planning
45–55 min
How training really works, risks, guardrails, and a decision guide
55–60 min
Takeaways and open discussion
DRL FOR RAN PLANNING & OPTIMIZATION
2

## Slide 3
03
MOTIVATION
Why AI Is Entering RAN Now
▸ Complexity has outgrown manual tuning. Multi-band, multi-vendor, massive MIMO, and dense small cells create far more tunable parameters than a team can hand-tune.
▸ Rule-based SON hits a ceiling. Static thresholds handle known patterns, but not the combinatorial interactions across thousands of cells.
▸ 5G/6G add new control dimensions. Beamforming, energy targets, network slicing, and sensing all need coordinated, not isolated, tuning.
SCALE OF THE PROBLEM
1000s
of cells per market, each with dozens of tunable parameters
24/7
traffic patterns that shift hourly, daily, and seasonally
Multi-cell
tradeoffs a single-cell fix can't see (coverage vs. interference)
DRL FOR RAN PLANNING & OPTIMIZATION
3

## Slide 4
04
THE GAP
The Limits of Traditional RAN Optimization
▸ Reactive, not consequential. Rule-based SON and legacy ML respond to known patterns — they don't learn the downstream effect of an action.
▸ Blind to delayed tradeoffs. Traditional tools optimize what they can see right now, not what happens two rings of cells later.
A FAMILIAR EXAMPLE
You boost power to fix a coverage hole. SINR improves locally — problem solved, according to the rule. But two rings of cells out, interference quietly rises, degrading throughput for neighbors the rule never looked at.
DRL FOR RAN PLANNING & OPTIMIZATION
4

## Slide 5
05
FOUNDATIONS
What Is Reinforcement Learning? (Plain-Language Loop)
Agent
The optimization controller making decisions
Environment
The live or simulated RAN — cells, UEs, traffic
State
What it observes: SINR, PRB load, throughput, latency, handovers
Action
A parameter it changes: tilt, power, HO offset, sched. weight
Reward
A score for network health: throughput ↑, drops ↓, energy ↓
The loop: observe → act → get scored → learn → repeat — thousands of times in simulation before ever touching a live network.
DRL FOR RAN PLANNING & OPTIMIZATION
5

## Slide 6
06
FOUNDATIONS
Simple RL vs. Deep RL
Simple (Tabular) RL
▸ Keeps a lookup table: one best action per state
▸ Works only for small, discrete problems
▸ Examples: Q-learning, SARSA, Monte Carlo
▸ Breaks down once state space gets large
Deep RL
▸ Replaces the table with a neural network
▸ Generalizes across states it hasn't exactly seen
▸ Examples: DQN, PPO, and others
▸ Needed the moment state is large or continuous — which is basically always in real RAN data
DRL FOR RAN PLANNING & OPTIMIZATION
6

## Slide 7
07
FOUNDATIONS
Two Families of DRL Algorithms
DISCRETE CHOICES
DQN
Picks the best option from a fixed menu of actions
CONTINUOUS CONTROL
PPO
Outputs a precise value and updates behavior gradually and safely
Both learn from trial and error in simulation — they differ in the shape of the action they produce.
DRL FOR RAN PLANNING & OPTIMIZATION
7

## Slide 8
08
DQN
DQN Explained Simply
DQN (Deep Q-Network) learns to answer one question: “Given this network state, which of my available discrete actions has historically led to the best long-term outcome?”
BEST SUITED TO
▸ Categorical, discrete decisions — not fine continuous values
▸ A fixed, enumerable menu of choices at each step
▸ Situations where 'which one' matters more than 'how much'
DRL FOR RAN PLANNING & OPTIMIZATION
8

## Slide 9
09
DQN
DQN Use Cases in RAN Planning & Optimization
Cell sleep mode
Turn a carrier or cell ON/OFF for energy saving in low traffic
Beam index selection
Choose one of a fixed set of beamforming codebook entries
Discrete power steps
Pick a power level from a preset list (e.g., 5 fixed steps)
Admission control
Admit, queue, or reject a new session
Handover target
Select which neighboring cell to hand a UE to
Scheduling tier
Choose a discrete MCS / priority tier
DRL FOR RAN PLANNING & OPTIMIZATION
9

## Slide 10
10
PPO
PPO Explained Simply
PPO (Proximal Policy Optimization) outputs a continuous number directly — the exact tilt, exact power in dBm, exact resource split — rather than choosing from a menu.
WHY “PROXIMAL” MATTERS
▸ It constrains how much the policy can change in one update
▸ Stays close to the last known-good behavior — no erratic swings
▸ Critical in live networks, where a bad update has real consequences
DRL FOR RAN PLANNING & OPTIMIZATION
10

## Slide 11
11
PPO
PPO Use Cases in RAN Planning & Optimization
Antenna tilt (CCO)
Continuous tilt optimization for coverage & capacity
Transmit power control
Fine-grained per-cell / per-beam power adjustment
Massive MIMO beams
Beam weight and beam-steering optimization
Energy scaling
Continuous power/PRB scaling with load, not hard on/off
Mobility (MRO)
Tuning HO margins, time-to-trigger, hysteresis
Load balancing
Weights across carriers, bands, or RATs (5G/Wi-Fi)
DRL FOR RAN PLANNING & OPTIMIZATION
11

## Slide 12
PART THREE
Five Use Cases, Deep Dive
Coverage · Mobility · Energy · Interference · Planning

## Slide 13
12
DEEP DIVE
Coverage & Capacity Optimization (CCO)
TYPICALLY PPO
The agent learns to balance coverage holes against overshoot interference across a whole cluster of cells — something single-cell tilt optimization can't do, because it never sees the multi-cell coupling that continuous tilt and power changes create.
DRL FOR RAN PLANNING & OPTIMIZATION
12

## Slide 14
13
DEEP DIVE
Mobility Robustness Optimization (MRO)
TYPICALLY PPO
Reduces ping-pong handovers, too-early/too-late handovers, and radio link failures by learning handover parameters per cell-pair from real mobility patterns — instead of one fixed threshold applied everywhere.
DRL FOR RAN PLANNING & OPTIMIZATION
13

## Slide 15
14
DEEP DIVE
Energy Savings
DQN + PPO
Balances energy consumption against QoS by learning when to sleep carriers/cells (DQN) or continuously scale massive MIMO power (PPO) — adapting to each site's actual daily and weekly traffic rhythm rather than a fixed time-based schedule.
DRL FOR RAN PLANNING & OPTIMIZATION
14

## Slide 16
15
DEEP DIVE
Interference Management
TYPICALLY PPO
Learns per-cell power and PRB allocation patterns that reduce inter-cell interference in dense deployments — especially relevant for small-cell clusters and C-band rollouts where classical ICIC struggles to coordinate across many neighbors.
DRL FOR RAN PLANNING & OPTIMIZATION
15

## Slide 17
16
DEEP DIVE
Network Planning Assistance
SIMULATION-DRIVEN
DRL agents trained inside digital twins/simulators rapidly evaluate ‘what if’ site placement, tilt, and power configurations before rollout — compressing planning cycles that used to require manual, iterative drive-testing.
DRL FOR RAN PLANNING & OPTIMIZATION
16

## Slide 18
17
LOOKING AHEAD
6G: What Changes, What Doesn't
▸ Extreme massive MIMO / sub-THz Beam management at a scale manual tuning can't reach
▸ Integrated Sensing & Communication (ISAC) Joint control of sensing and communication parameters
▸ Reconfigurable Intelligent Surfaces (RIS) Phase-shift optimization across surface elements
All three are naturally continuous control problems — a strong fit for PPO-family methods.
DRL FOR RAN PLANNING & OPTIMIZATION
17

## Slide 19
18
IN PRACTICE
How Training Actually Works
1. Simulate
Train offline in a simulator or digital twin using historical or synthetic traffic — never directly on the live network
2. Validate
Extensive testing in simulation before any real-world exposure
3. Shadow mode
Deployed live but only observing and recommending — not acting
4. Canary rollout
Small cluster deployment, engineers monitoring with rollback ready
Human engineers stay in the loop at every stage, with authority to roll back at any point.
DRL FOR RAN PLANNING & OPTIMIZATION
18

## Slide 20
19
GUARDRAILS
Risks and Practical Guardrails for RF Engineers
▸ Reward shaping pitfalls A poorly designed reward can optimize the wrong thing — e.g., maximizing throughput while ignoring energy or fairness
▸ Hard safety bounds Guardrails so the agent can't take extreme actions, like power hard limits
▸ Explainability Engineers need visibility into why an action was taken, not a black box
▸ Fallback to rules Revert to rule-based control if the agent behaves unexpectedly
▸ Drift monitoring Watch for performance decay as traffic patterns change over time
DRL FOR RAN PLANNING & OPTIMIZATION
19

## Slide 21
20
DECISION GUIDE
DQN vs. PPO — Quick Reference
DQN
PPO
Control variable
Discrete / categorical
Continuous / fine-grained
Example
Which cell, which beam index, on/off
Exact power, exact tilt, exact ratio
Update style
Selects from a fixed menu
Smooth, bounded, gradual updates
Best fit for
Simpler sandbox problems first
Production-adjacent, safety-critical rollout
DRL FOR RAN PLANNING & OPTIMIZATION
20

## Slide 22
21
SUMMARY
Key Takeaways
▸ DRL is disciplined trial-and-error, not magic. It outperforms static rules in complex, multi-cell, multi-objective RAN environments.
▸ DQN suits discrete decisions; PPO suits continuous, fine-grained, safer control.
▸ Success depends more on reward design and staged rollout than on algorithm choice alone.
▸ Start bounded. Pick one well-instrumented use case — energy savings or tilt optimization — before attempting network-wide control.
DRL FOR RAN PLANNING & OPTIMIZATION
21

## Slide 23
OPEN DISCUSSION
Questions & Discussion
Which of your current manual tuning tasks looks most like a DQN problem — and which looks more like a PPO problem?