## Slide 1
A ONE-HOUR TECHNICAL SESSION FOR RF & RAN ENGINEERS
Deep Reinforcement Learning for RAN Planning & Optimization
How DQN and PPO learn to tune coverage, capacity, mobility, interference, and energy the way an experienced RF engineer would — explained without the math.
Dr Rao S Yenamandra · DigitalTwinSim
60 MINUTES · 29 TOPICS · LIGHT ON MATH, HEAVY ON INTUITION

## Slide 2
02
AGENDA
What We'll Cover in 60 Minutes
00–10 min
Why RAN optimization needs AI now, and what RL actually is
10–25 min
DQN and PPO explained simply, with RAN use cases for each
25–45 min
Deep dives: coverage & capacity, mobility, energy, interference, planning
45–55 min
How training really works, risks, guardrails, and a decision guide
55–60 min
Takeaways and open discussion
DRL FOR RAN PLANNING & OPTIMIZATION
2

## Slide 3
03
MOTIVATION
Why AI Is Entering RAN Now
▸ Complexity has outgrown manual tuning. Multi-band, multi-vendor, massive MIMO, and dense small cells create far more tunable parameters than a team can hand-tune.
▸ Rule-based SON hits a ceiling. Static thresholds handle known patterns, but not the combinatorial interactions across thousands of cells.
▸ 5G/6G add new control dimensions. Beamforming, energy targets, network slicing, and sensing all need coordinated, not isolated, tuning.
SCALE OF THE PROBLEM
1000s
of cells per market, each with dozens of tunable parameters
24/7
traffic patterns that shift hourly, daily, and seasonally
Multi-cell
tradeoffs a single-cell fix can't see (coverage vs. interference)
DRL FOR RAN PLANNING & OPTIMIZATION
3

## Slide 4
04
THE GAP
The Limits of Traditional RAN Optimization
▸ Reactive, not consequential. Rule-based SON and legacy ML respond to known patterns — they don't learn the downstream effect of an action.
▸ Blind to delayed tradeoffs. Traditional tools optimize what they can see right now, not what happens two rings of cells later.
A FAMILIAR EXAMPLE
You boost power to fix a coverage hole. SINR improves locally — problem solved, according to the rule. But two rings of cells out, interference quietly rises, degrading throughput for neighbors the rule never looked at.
DRL FOR RAN PLANNING & OPTIMIZATION
4

## Slide 5
05
FOUNDATIONS
What Is Reinforcement Learning? (Plain-Language Loop)
Agent
The optimization controller making decisions
Environment
The live or simulated RAN — cells, UEs, traffic
State
What it observes: SINR, PRB load, throughput, latency, handovers
Action
A parameter it changes: tilt, power, HO offset, sched. weight
Reward
A score for network health: throughput ↑, drops ↓, energy ↓
The loop: observe → act → get scored → learn → repeat — thousands of times in simulation before ever touching a live network.
DRL FOR RAN PLANNING & OPTIMIZATION
5

## Slide 6
06
FOUNDATIONS
The RL Loop, in a Few Simple Equations
State
s_t = ( SINR_t, PRB_t, Thpt_t, Lat_t, ... )
A snapshot of network conditions the agent observes at time t
Action
DQN: a_t ∈ {a₁, ..., aₙ} | PPO: a_t ∈ [a_min, a_max]
A discrete pick (DQN) or a precise continuous value (PPO)
Reward
r_t = w₁·Throughput_t − w₂·Drops_t − w₃·Energy_t
A weighted KPI score — same idea as a weighted scorecard engineers already use
Penalty
r_t′ = r_t − λ·Violation(a_t)
Subtracts a cost whenever an action breaks an operating rule
Guardrail
a_t = clip( a_t , a_min , a_max )
Hard-clamps the action so it can never leave a safe operating range
Objective
G_t = Σ γᵏ · r_{t+k} (k = 0 → ∞)
What the agent is really maximizing: reward now plus discounted future reward
None of this runs by hand — the network learns the weights and bounds through simulation. This is just the shape of what it's learning.
DRL FOR RAN PLANNING & OPTIMIZATION
6

## Slide 7
07
FOUNDATIONS
The RAN as a Multi-Step Decision Process (MDP)
An MDP is just a formal name for “a sequence of decisions where each one shapes the next.” Formally: (S, A, P, R, γ) — states, actions, transitions, rewards, and a discount factor.
s₀
a₀
s₁, r₁
a₁
s₂, r₂
a₂
s₃, r₃
TWO IDEAS THAT MATTER IN PRACTICE
▸ Markov property: s_{t+1} depends only on s_t and a_t — the agent doesn't need the network's entire history, just its current reading.
▸ Credit assignment: a tilt or power change now may not show its full effect for several steps — handover patterns and interference settle over minutes. γ (from the equations slide) is what lets the agent value that delayed payoff.
DRL FOR RAN PLANNING & OPTIMIZATION
7

## Slide 8
08
FOUNDATIONS
Simple RL vs. Deep RL
Simple (Tabular) RL
▸ Keeps a lookup table: one best action per state
▸ Works only for small, discrete problems
▸ Examples: Q-learning, SARSA, Monte Carlo
▸ Breaks down once state space gets large
Deep RL
▸ Replaces the table with a neural network
▸ Generalizes across states it hasn't exactly seen
▸ Examples: DQN, PPO, and others
▸ Needed the moment state is large or continuous — which is basically always in real RAN data
DRL FOR RAN PLANNING & OPTIMIZATION
8

## Slide 9
09
FOUNDATIONS
Two Families of DRL Algorithms
DISCRETE CHOICES
DQN
Picks the best option from a fixed menu of actions
CONTINUOUS CONTROL
PPO
Outputs a precise value and updates behavior gradually and safely
Both learn from trial and error in simulation — they differ in the shape of the action they produce.
DRL FOR RAN PLANNING & OPTIMIZATION
9

## Slide 10
10
DQN
DQN Explained Simply
DQN (Deep Q-Network) learns to answer one question: “Given this network state, which of my available discrete actions has historically led to the best long-term outcome?”
BEST SUITED TO
▸ Categorical, discrete decisions — not fine continuous values
▸ A fixed, enumerable menu of choices at each step
▸ Situations where 'which one' matters more than 'how much'
DRL FOR RAN PLANNING & OPTIMIZATION
10

## Slide 11
11
DQN
DQN Use Cases in RAN Planning & Optimization
Cell sleep mode
Turn a carrier or cell ON/OFF for energy saving in low traffic
Beam index selection
Choose one of a fixed set of beamforming codebook entries
Discrete power steps
Pick a power level from a preset list (e.g., 5 fixed steps)
Admission control
Admit, queue, or reject a new session
Handover target
Select which neighboring cell to hand a UE to
Scheduling tier
Choose a discrete MCS / priority tier
DRL FOR RAN PLANNING & OPTIMIZATION
11

## Slide 12
12
DQN
DQN: Choosing Inputs and Outputs
INPUTS (STATE FEATURES)
▸ PRB utilization (%) for this cell and neighbors
▸ Active UE count and traffic mix
▸ Time of day / day-of-week traffic trend
▸ Current SINR and interference readings
OUTPUT — ONE Q-VALUE PER DISCRETE ACTION
Example action menu: {Stay Awake, Sleep 1 Carrier, Sleep 2 Carriers}
Q = [ 0.82, 0.91, 0.34 ]
Agent picks the highest-scoring action
action = argmax(Q) → Sleep 1 Carrier
Design choice for DQN: the input is a feature vector; the output layer has exactly one node per possible action. Adding a new action means adding a new output node and retraining.
DRL FOR RAN PLANNING & OPTIMIZATION
12

## Slide 13
13
PPO
PPO Explained Simply
PPO (Proximal Policy Optimization) outputs a continuous number directly — the exact tilt, exact power in dBm, exact resource split — rather than choosing from a menu.
WHY “PROXIMAL” MATTERS
▸ It constrains how much the policy can change in one update
▸ Stays close to the last known-good behavior — no erratic swings
▸ Critical in live networks, where a bad update has real consequences
BEST SUITED TO
▸ Continuous, fine-grained values — not a fixed menu of choices
▸ Smooth, gradual adjustment toward a target setting
▸ Situations where 'how much' matters more than 'which one'
DRL FOR RAN PLANNING & OPTIMIZATION
13

## Slide 14
14
PPO
Weighting the PPO Reward by KPI Importance
PPO doesn’t optimize each KPI on its own — it maximizes one weighted score. Every input KPI carries a weight set by its importance to the slice SLA, so re-weighting the reward re-points the same agent at a new objective.
EXAMPLE — eMBB REWARD WEIGHTS
Throughput — w ≈ 0.35 · primary eMBB SLA target
PRB / spectral efficiency — w ≈ 0.25 · capacity headroom
SINR margin — w ≈ 0.20 · link quality
Energy per bit — w ≈ 0.12 · OPEX
Latency — w ≈ 0.08 · eMBB tolerates delay — weighted last
Weights are chosen in reward design (see slide 6) — set by engineers, not learned.
SAME KPIs, DIFFERENT SLICE
▸ URLLC — latency and reliability jump to the top; throughput weight drops down the list
▸ mIoT — admission fairness and energy dominate; throughput weight falls near zero
▸ The weights encode the SLA — the state and action design never change
DRL FOR RAN PLANNING & OPTIMIZATION
14

## Slide 15
15
PPO
PPO Use Cases in RAN Planning & Optimization
Antenna tilt (CCO)
Continuous tilt optimization for coverage & capacity
Transmit power control
Fine-grained per-cell / per-beam power adjustment
Massive MIMO beams
Beam weight and beam-steering optimization
Energy scaling
Continuous power/PRB scaling with load, not hard on/off
Mobility (MRO)
Tuning HO margins, time-to-trigger, hysteresis
Load balancing
Weights across carriers, bands, or RATs (5G/Wi-Fi)
DRL FOR RAN PLANNING & OPTIMIZATION
15

## Slide 16
16
PPO
PPO: Choosing Inputs and Outputs
INPUTS (STATE FEATURES)
▸ SINR distribution across the sector
▸ Throughput, latency, and drop-rate trends
▸ Interference reported by neighboring cells
▸ Current tilt / power setting (so it knows its starting point)
OUTPUT — A DISTRIBUTION OVER A CONTINUOUS VALUE
The network outputs a mean and a spread, not one fixed number
μ = 4.2°, σ = 0.3°
Training samples from it (exploration); inference just takes the mean
a_t ~ N(μ, σ) → a_t = μ
In plain terms: μ is the value the policy settled on, and σ is how far it explores around μ while training — at deployment it just uses μ.
Design choice for PPO: the output layer has two nodes per continuous action (its mean and spread) instead of one node per menu item — that's what lets it express “tilt down by 4.2°” instead of only choosing from a fixed list.
DRL FOR RAN PLANNING & OPTIMIZATION
16

## Slide 17
17
ARCHITECTURE
Custom Neural Network vs. Open-Source SLM as the Policy Backbone
Custom Neural Network
▸ Small MLP/CNN trained from scratch directly on numeric KPI vectors
▸ Thousands to low millions of parameters
▸ Inference in microseconds — fits inline in a real-time control loop
▸ Trained purely from the reward signal (DQN/PPO) — no language understanding
Open-Source SLM
▸ Pretrained small language model (e.g. Llama, Phi, Mistral-class) repurposed as a decision layer
▸ Billions of parameters — orders of magnitude larger
▸ Inference in tens to hundreds of milliseconds — too slow for a tight per-TTI loop
▸ Brings general reasoning and can explain its decision in plain language
Rule of thumb: use a custom NN for the fast, precise, numeric control loop itself (tilt, power, admission, sleep). An SLM fits better one layer up — reading alarms/tickets in natural language and deciding which specialized DQN/PPO policy to invoke, or explaining a decision to an engineer.
DRL FOR RAN PLANNING & OPTIMIZATION
17

## Slide 18
PART THREE
Five Use Cases, Deep Dive
Coverage · Mobility · Energy · Interference · Planning

## Slide 19
18
DEEP DIVE
Coverage & Capacity Optimization (CCO)
TYPICALLY PPO
The agent learns to balance coverage holes against overshoot interference across a whole cluster of cells — something single-cell tilt optimization can't do, because it never sees the multi-cell coupling that continuous tilt and power changes create.
DRL FOR RAN PLANNING & OPTIMIZATION
18

## Slide 20
19
DEEP DIVE
Mobility Robustness Optimization (MRO)
TYPICALLY PPO
Reduces ping-pong handovers, too-early/too-late handovers, and radio link failures by learning handover parameters per cell-pair from real mobility patterns — instead of one fixed threshold applied everywhere.
DRL FOR RAN PLANNING & OPTIMIZATION
19

## Slide 21
20
DEEP DIVE
Energy Savings
DQN + PPO
Balances energy consumption against QoS by learning when to sleep carriers/cells (DQN) or continuously scale massive MIMO power (PPO) — adapting to each site's actual daily and weekly traffic rhythm rather than a fixed time-based schedule.
DRL FOR RAN PLANNING & OPTIMIZATION
20

## Slide 22
21
DEEP DIVE
Interference Management
TYPICALLY PPO
Learns per-cell power and PRB allocation patterns that reduce inter-cell interference in dense deployments — especially relevant for small-cell clusters and C-band rollouts where classical ICIC struggles to coordinate across many neighbors.
DRL FOR RAN PLANNING & OPTIMIZATION
21

## Slide 23
22
DEEP DIVE
Network Planning Assistance
SIMULATION-DRIVEN
DRL agents trained inside digital twins/simulators rapidly evaluate ‘what if’ site placement, tilt, and power configurations before rollout — compressing planning cycles that used to require manual, iterative drive-testing.
DRL FOR RAN PLANNING & OPTIMIZATION
22

## Slide 24
23
LOOKING AHEAD
6G: What Changes, What Doesn't
▸ Extreme massive MIMO / sub-THz Beam management at a scale manual tuning can't reach
▸ Integrated Sensing & Communication (ISAC) Joint control of sensing and communication parameters
▸ Reconfigurable Intelligent Surfaces (RIS) Phase-shift optimization across surface elements
All three are naturally continuous control problems — a strong fit for PPO-family methods.
DRL FOR RAN PLANNING & OPTIMIZATION
23

## Slide 25
24
IN PRACTICE
Training Phase vs. Inference Phase
Training Phase
▸ Agent explores — takes some random / noisy actions on purpose
▸ Experience is collected: a replay buffer (DQN) or rollout trajectories (PPO)
▸ A loss is computed (TD-error for DQN, clipped surrogate objective for PPO) and weights are updated by backpropagation
▸ Runs for many simulated episodes — hours to days, on GPU compute, entirely offline
Inference Phase
▸ Weights are frozen — no more learning happens on the fly
▸ Exploration is switched off: the agent takes its best-known action (argmax for DQN, the mean μ for PPO)
▸ Just one forward pass through the network per decision
▸ Runs in milliseconds on modest compute — suitable for a live RIC control loop
DRL FOR RAN PLANNING & OPTIMIZATION
24

## Slide 26
25
IN PRACTICE
How Do You Know It Converged?
Convergence = training has stopped meaningfully improving the policy.
▸ Reward curve flattens. Episode return climbs, then plateaus instead of still trending up.
▸ Loss stabilizes. TD-error (DQN) or policy loss (PPO) decreases and levels off near a small value.
▸ Policy stops changing much between updates. PPO's own clipping is built around bounding this step-to-step change.
▸ Validation KPIs hold steady across independent runs. Simulated throughput / drop-rate / energy stop drifting run to run.
Watch the curve, don't trust a fixed iteration count — a flat reward can also mean the agent settled into a local optimum, not the best possible policy. Validate against varied traffic scenarios before trusting it.
DRL FOR RAN PLANNING & OPTIMIZATION
25

## Slide 27
26
IN PRACTICE
How Training Actually Works
1. Simulate
Train offline in a simulator or digital twin using historical or synthetic traffic — never directly on the live network
2. Validate
Extensive testing in simulation before any real-world exposure
3. Shadow mode
Deployed live but only observing and recommending — not acting
4. Canary rollout
Small cluster deployment, engineers monitoring with rollback ready
Human engineers stay in the loop at every stage, with authority to roll back at any point.
DRL FOR RAN PLANNING & OPTIMIZATION
26

## Slide 28
27
GUARDRAILS
Risks and Practical Guardrails for RF Engineers
▸ Reward shaping pitfalls A poorly designed reward can optimize the wrong thing — e.g., maximizing throughput while ignoring energy or fairness
▸ Hard safety bounds Guardrails so the agent can't take extreme actions, like power hard limits
▸ Explainability Engineers need visibility into why an action was taken, not a black box
▸ Fallback to rules Revert to rule-based control if the agent behaves unexpectedly
▸ Drift monitoring Watch for performance decay as traffic patterns change over time
DRL FOR RAN PLANNING & OPTIMIZATION
27

## Slide 29
28
CASE STUDY
Guarded DQN vs. Guarded PPO — a Real PRACH Storm Result
PRACH storm mitigation: synchronized mIoT devices flood the random-access channel, collide on preambles, and retry — a real overload scenario, not a toy problem.
THE SHARED GUARD
Admission ceiling ∝ 0.90M/B_t caps how wide either agent can open access | Recovery floor ∝ 0.35M/B_t stops either agent from throttling forever while idle
Guarded DQN
Guarded PPO
Success rate (3,000-device storm)
100%
99.8%
Failures
0
7
95th-pct. delay
18.6 s
22.2 s
Held-out scenarios won (of 30)
20
0
Read carefully: both controllers shared the identical guard, state, reward, and training storms — this favors DQN within this shared guard on a 13-action discrete PRACH control problem, not a general claim that DQN beats PPO. Guard-only and unguarded ablations are still future work.
DRL FOR RAN PLANNING & OPTIMIZATION
28

## Slide 30
29
DECISION GUIDE
DQN vs. PPO — Quick Reference
DQN
PPO
Control variable
Discrete / categorical
Continuous / fine-grained
Example
Which cell, which beam index, on/off
Exact power, exact tilt, exact ratio
Update style
Selects from a fixed menu
Smooth, bounded, gradual updates
Best fit for
Simpler sandbox problems first
Production-adjacent, safety-critical rollout
DRL FOR RAN PLANNING & OPTIMIZATION
29

## Slide 31
30
SUMMARY
Key Takeaways
▸ DRL is disciplined trial-and-error, not magic. It outperforms static rules in complex, multi-cell, multi-objective RAN environments.
▸ DQN suits discrete decisions; PPO suits continuous, fine-grained, safer control.
▸ Success depends more on reward design and staged rollout than on algorithm choice alone.
▸ Start bounded. Pick one well-instrumented use case — energy savings or tilt optimization — before attempting network-wide control.
DRL FOR RAN PLANNING & OPTIMIZATION
30

## Slide 32
OPEN DISCUSSION
Questions & Discussion
Which of your current manual tuning tasks looks most like a DQN problem — and which looks more like a PPO problem?